## Slide 1: Non-gravitational Forces on Satellites at GEO: Advances, Techniques and Challenges
Professor Marek Ziebart
Chair, IGS Satellite Vehicle Orbit Dynamics Working Group
NATO SCI-279 Task Group
Director, Space Geodesy and Navigation Laboratory
University College London
EOARD SSA Workshop, Ruislip, United Kingdom December 7th, 2016

## Slide 2
SV state and track custody: Problem Elements
Reference frame
Dynamics
Measurements,
Measurement models
Integrator
Estimator
State/track uncertainty
Notes: Track custody: the ability to establish and maintain unique space object identification. Absolute track custody implies eliminating the possibility of mistaken identification and always knowing where the space object is and will be over operationally relevant time scales.

## Slide 3
Forces acting on an orbiter
PRP
(planetary radiation
pressure)
Lunar gravity
planetary gravity
general relativistic
effects
Earth gravity
Solar gravity
Tidal effects
Solar radiation pressure (SRP)
Thermal forcing
(TRR)
Antenna thrust
(AT)
Particulates drag,
Solar wind
Lorentz forcing
Out-gassing
Notes: 3
For the GNSS altitude we conventionally assume that the conservative gravitational effects are very well known – particularly since the launch and analysis of dedicated gravity field missions like GRACE and GOCE. The radiation pressure effects are perceived as more problematic and simplified, empirical approaches are adopted.

## Slide 4: We can categorize these forces using four fields:
Gravitational potential
Electro-magnetic radiation
Particulate matter
Geomagnetic

## Slide 5: Photons and Radiation Pressure

## Slide 6: Everyone knows….......
Momentum!
For Photons:
ρ=E/c
Momentum = Energy/speed of light
Radiation Pressure
Notes: Special relativity says e = m c squared – but Einstein went further than that energy is related to mass and momentum. Photons have a zero rest mass so we rearrange the equation and see that photons carry momentum. When they hit something – it moves!

## Slide 7
Resultant force
Radiation Pressure
Notes: All this science in some way depends on knowing where the spacecraft is in space…….. And that is what we are going to consider

## Slide 8: Modelling philosophy
Utilise all available physical and engineering data about the space vehicle and the space environment to build force models
Embrace the complexity of the processes
Develop models that capture the complexity, but that run fast in implementation
Heritage established through nearly 20 years of mission experience (JPL, GSFC, USAF, ESA)
UCL models used as operational standards for several NASA missions and for all science grade GPS orbit products

## Slide 9
We develop a detailed structural computer model of the spacecraft

## Slide 10: Ray Tracing - 1
Spacecraft model represented in the SV body frame
Geometry
Optical and thermal properties
Material types
Notes: Spacecraft bus, we generally separate out the solar panels as hey can be treated as flat plates analytically

## Slide 11: Ray Tracing - 2
An array of flux origin points is created
Dependent on the incoming flux direction
Notes: So we choose a incoming flux direction
Align a grid of points in a plane perpendicular to this direction

## Slide 12: Ray Tracing - 3
Rays are generated from each of these points
Notes: Propagated towards the spacecraft

## Slide 13: Ray Tracing - 4
The intersection between each ray and the spacecraft is computed

## Slide 14: Ray Tracing - 5
The material properties of the surface are known at each of these points

## Slide 15: Ray Tracing - 6
The surface normal is calculated at each of these points for planar or curved surfaces
Notes: Mention Curved Surfaces

## Slide 16: Ray Tracing - 7
New rays are generated for each reflection and the intersection and reflection step repeated:
Secondary intersections

## Slide 17: Ray Tracing - 8
The acceleration data for all rays (primary and secondary) is collected:
Resultant acceleration computed for that radiation source direction

## Slide 18: Process is repeated for other incoming flux directions

## Slide 24: Summary of modelling techniques
Photon pressure modelling of complex forms through ray tracing
Flux models (solar, Earth radiation)
SV thermal effects (MLI, solar panel thermal gradient, radiator output)
Antenna thrust
Mass history modelling
Surface charge analysis via photo-electric effect*
Lorentz forcing*
Torque analysis*
* Research topics – everything else has flight heritage

## Slide 25
How well do these ideas work? Do they make any difference?:
Predicting a GPS satellite orbit over a 173,000 km trajectory

## Slide 26
-2
0
2
4
6
8
10
0
1
2
3
4
5
6
7
8
9
10
11
12
Time (hours)
Orbit Prediction Error (m)
Solar radiation pressure (SRP) only
SRP + Thermal force (TRR)
SRP + TRR + Antenna Thrust (AT)
SRP + TRR + AT + Planetary Radiation Pressure
Along-track orbit prediction errors over 12 hours for one GPS IIR satellite with different photon-based force models
8 metre
orbit error
Notes: Animate the build up of sophistication

## Slide 27: Sensitivity to surface forces: Area to mass ratio

## Slide 28: Typical space vehicle characteristics

## Slide 29: Characteristic Solar Pressure Accelerations for LEO, MEO and GEO satellites

## Slide 30: Key Point 1:
GEO Satellites are highly sensitive to surface force effects compared to LEO/MEO satellites
Double Whammy: gravity weak, surface forces strong

## Slide 31: Key Point 2:
Precision surface force modelling techniques developed for MEO/LEO missions have not been applied to GEO space vehicles as yet

## Slide 32
Lorentz Force Effects
An object in orbit carrying a net electrostatic charge (Q), will be influenced by an interaction with the local electromagnetic field, due to the Lorentz force.
Q
v
B (magnetic flux density)
magnetic flux tube
F = QvxB
Notes: The magnetic component of the Lorentz force, the vxB, is always orthogonal to the instantaneous velocity vector.

## Slide 33
Magnitudes of the standard case GLA (equatorial plane: z = 0),
17 July 2013
Geostationary
Orbit
in ms-2
0
-5
5
x/RE
y/RE
0
-5
5
y
x
z
RE is the
mean Earth radius
The standard case:
m = 1 kg
q = 1 Coulomb
Thus, q/m = 1 C/kg
Circular orbit
Inclination = 0
2000 km – ~36,000 km
sample
velocity vector
Notes: We’ve developed a way of studying the Lorentz force effects by examining vxB maps.
For an object in orbit, the geomagnetic Lorentz force would be scaled by the Q(r,v,t).
These are standard Lorentz force maps.
Circular orbits.
Mass 1kg
Carrying 1 coulomb charge.
The force/accelerations are stronger closer to the Earth. However, there are distinct feature, and non-zero accelerations up to GEO.

## Slide 34: Lorentz force at GEO
SVs co-rotating with the Earth have minimal velocity with respect to field
In super-GEO or geo-synchronous effects could be more pronounced (graveyard effects)
Key parameter is Q/m (charge to mass ratio)
Knowledge of charging is limited (currently)
Effect would be systematic (e.g. an issue for graveyard orbits)
It leads to another interesting question: solar wind and the plasma environment

## Slide 35: Thoughts/Questions over the GEO Environment
Particulate radiation environment is difficult to predict a priori – take measurements?
Solar wind modelling and prediction – ingest predictive, space weather data from L2?
Engage with the space weather community for the purposes of dynamics modelling?
Commercial satellite operators (via NATO SCI TG) are willing to host instruments ‘on the wings’
A useful resource is the experience of existing satellite operators
Consider using a GEO satellite exploiting GPS side lobes for positioning

## Slide 36: Conclusions
Non-gravitational orbital dynamics at GEO are unique and relatively unexplored (radiation pressure, solar wind, Lorentz)
GEO satellites have very high area-to-mass ratios compared to LEO/MEO SVs: sensitive to surface force effects
Mature modelling techniques (LEO/MEO) not yet applied to GEO
Environmental effects (plasma fields, solar wind forcing, charging, Lorentz) are poorly understood – may require sensor development on orbit
It would be useful to carry out a study on GEO orbital dynamics to quantify just what ‘natural motion’ comprises and to ingest new sensor information
This could provide the basis for track custody developments – identification and trajectory prediction

## Slide 37: Back up slides

## Slide 38: Total solar irradiance and sunspot number

## Slide 39: Spiral points computation
10,000 pixel arrays distributed evenly over a sphere centred on the S/C bus
1mm pixel resolution
Each pixel array position yields a resultant radiation force vector in body-frame components
Primary data set from which the grid file calculation is derived
The grid file allows for interpolation to create a continuous acceleration surface, modelled in the S/C body frame

## Slide 40
UCL Computational Efficiency & Quality Control

## Slide 41
UCL Computational Efficiency & Quality Control

## Slide 42: Thermal modelling: Anisotropic thermal emission from spacecraft results in a net acceleration
heat
heat
heat
heat
recoil
recoil
recoil
recoil
Determine temperature distribution
Derive recoil force

## Slide 43
Multilayer Insulation (MLI)
To s/c
Emitted
radiation
Incoming
radiation (W) absorbed
Energy balance:
Pixel array algorithm determines insolation of MLI
‘Effective emissivity’ (eeff) parameter governs heat transfer to bus
MLI blackened, a=0.94  large thermal force
Thermally
stabilised
bus, Tsc
q
Notes: This is to try to keep spacecraft thermally stable.
MLI is designed to transport very little heat through to spacecraft
Effetive emissivity derived experimentally

## Slide 44: Solar Panel Thermal Analysis
Steady state and transient models (during eclipse) developed to yield temperatures and forces
Input data : thicknesses and conductivities of panel composite layers, surface emissivities and absorptivities, power draw
Model verification by comparison with telemetered surface temperatures

## Slide 45: Solar panel thermal gradient force: system
Tf
T1
T2
…..
Tb
Tn
Temperatures
K1
K2
Kn
…..
Conductivities
Power draw
Emitted heat (rear face)
Emitted heat (front face)
Incoming radiation
(solar, Earth IR)
Incoming radiation
(Earth IR)
Dx (slab thicknesses)
Absorptivity (af)
Emissivity (ef)
Absorptivity (ab)
Emissivity (eb)

## Slide 46: Solar panel thermal gradient force: Inputs and outputs
Inputs:
Incident radiation fluxes
Panel attitude in inertial space
Absorptivity and emissivity (front and back)
Slab thicknesses and conductivities
Power draw
Outputs:
Intermediate:
  Temperatures at slab interfaces
  Net thermal gradient
Final:
  Accelerations due to thermal emission (front and back)

## Slide 47: Earth radiation: Emitted (LW) and reflected (SW) radiation

## Slide 48
Maximum SW flux: May 2004
Maximum SW flux: Dec 2003
400
200
0
600
Planetary Radiation Pressure (PRP)
SW Radiation Complexity – strong seasonal signals

## Slide 49: Modelling Earth radiation pressure step 1: Visibility of Satellite to Grid Cells
GPS SVN 44 at one epoch on 1st July 2001

## Slide 50
Modelling Earth radiation pressure step 2:
Compute reduction in flux as a function of satellite-cell elevation and satellite-cell distance

## Slide 51
Planetary radiation pressure HCL accelerations, GPS satellite SVN 41
H = Height C = Cross track L = aLong Track

## Slide 52: Orbit accuracy tests: Satellite Laser Ranging (SLR)
Range measurement from time of flight
Accuracy:
generally sub-centimetre
Ranging requires retro-reflectors
Laser pulse of photons

## Slide 53: GPS satellites carrying retro-reflectors
2 Block IIA spacecraft
PRN05, PRN06
Retro-reflector array

## Slide 54
True trajectory
(tracked by SLR)
Estimated orbit (e.g. IGS)
(from pseudo-range
and phase)
Mean bias
~ 5 cm
Estimated orbit is
consistently
too high
5cm range error => [gravity] acceleration error of: ~2.3x10-9 ms-2
Small number, big effect : along track error of ~2.11m (12 hrs)
The GPS-SLR Orbit Anomaly

## Slide 55
IGS combined
JPL nom PRP
JPL UCL PRP
SLR
5 cm
3.3 cm
2.9 cm
Combined Earth radiation pressure and antenna thrust model reduces SLR bias by 21 mm
Mean Orbit Differences

## Slide 56: Laser Retro-reflector Array (LRA) offset
LRA position in s/c body frame required for analysis of laser ranging
New data suggests LRA offset further from centre of mass than previously understood
Shim corrections: +11 mm (PRN05), +13 mm (PRN06)
shim

## Slide 57: IGS experiments, analysis, standards
This research leads to IGS standards – applied by all analysis groups within the organization. Ideas are tested by large-scale data processing experiments spanning many years and huge networks of data. The recent REPRO2 exercise re-computed orbit, clock, station positions and earth orientation parameters using over twenty years of daily data from the entire network. Such operations give insight into system and planet scale behaviors.
Earth radiation forcing and antenna thrust methods changed IGS orbit accuracy from 5 cm to 2.5 cm (radial)

## Slide 58: Phase centre variation method: Jason-1&2
Utilise many months of GPS observations
Stack phase residuals by bins as a function of latitude and longitude in antenna frame
Create look up table of phase observation corrections

## Slide 59: What do we need to do this, and to push the envelope of what is possible:
SV mass and mass history
Structural details (primarily surface geometry)
Material types (absorptivity, reflectivity, specularity)
Specific thermal information (MLI characteristics, power draw, thermal emissions, solar panel construction)
Satellite attitude (both eclipsing and non-eclipsing, non-nominal attitude, yaw flips, noon day and midnight turns)
Satellite phase centre (phase centre offset, phase centre variations)
Laser retro-reflector array position, corner cube phase centre

## Slide 60: Emerging Technology and Challenges
Many GNSS satellites carrying retro-reflectors (Galileo; GPS III, Beidou, GLONASS)
Galileo orbit and clock performance – a new benchmark?
Next generation understanding of the space environment (radiation fluxes, Lorentz forcing)
New paradigms in atmospheric density modelling
Accurate space vehicle phase centre information
Utilising telemetry in the OD/prediction process
Using measured attitude instead of attitude laws

## Slide 61
~1.02 degrees
708 km
~1.14 degrees
MEO:
Dynamics
Monopole
J2
Lorentz

## Slide 62: GPS 2.5cm orbit accuracy: summary
Precise knowledge of retro-reflector array position
Dynamics modelling: antenna thrust
Dynamics modelling: Earth radiation forcing
Careful calibration of receiver and satellite phase centres
Well defined reference frame and Earth orientation parameters
Sophisticated troposphere mapping functions and horizontal troposphere gradient parameters

## Slide 63: 1cm accuracy Jason-class orbit: summary
Careful calibration of GPS receiver phase centres and phase centre variations
Detailed modelling of solar radiation pressure and thermal re-radiation effects
Use of measured attitude (quaternions) over the attitude laws
High accuracy GPS orbits

## Slide 64: Why we need a 1cm orbit for Jason-class satellites: Global sea level rise measured by satellite altimetry

## Slide 65: Conclusions
Non-gravitational orbital dynamics at GEO are unique and relatively unexplored
GEO satellites have very high area-to-mass ratios compared to LEO/MEO SVs, making them particularly sensitive to surface force effects
Some environmental effects (plasma fields, solar wind forcing) are poorly understood – may require sensor development on orbit
It would be useful to carry out a study on GEO orbital dynamics to quantify just what ‘natural motion’ comprises
This would provide the basis for discrimination techniques

## Slide 66
Eclipse
Eclipse
Acceleration (ms-2)
Time (hours of day)
Height
Cross track
Along track
}
accelerations
Modelled Earth Radiation pressure (SVN35, UCL ADM model

## Slide 67
Thermal

## Slide 68
Thermal

## Slide 69
Thermal
Albedo

## Slide 70
Thermal
Albedo

## Slide 71
Thermal
Albedo

## Slide 73: Explanation
Orbit estimated using
using phase/pseudorange
(without modelling PRP)
Solar panel
‘SLR orbit’
Symmetric thermal thrust
Assymetric ‘Albedo’ thrust

## Slide 74
Star sensor
Becomes
visible
Maximum Y-acceleration
due to star sensors
Effect reduces as
profile changes
Opposing faces
cancel effect