## Slide 1: ACI Meeting 7th and 8th December 2016
Mike Trethewey Control Loop Concepts Ltd (CL2)

## Slide 2: Overview
CL2 Capability & Facilities
Networking of Sensors
GEO & MEO Observations
Work is part funded by STFC/DSTL contracts

## Slide 3: CL2 at STFC Chilbolton
Satellite IOT since 2005 (Giove A & Giove B)
Located at Chilbolton since 2010
EO Tracker platform development & testing
Satellite EO Observations since June 2014

## Slide 5: CL2 Tracking Involvement
Platform Development with Acuitas AG
  Control system design
  System Integrator
  Provision of real-time software
  Customer specials
Long Experience with Control System Design & Electro-Optical Auto-Trackers

## Slide 6: Acuitas Tracking Platforms Acuitas AG Alpendorf SZ Switzerland www.acuitas.ch

## Slide 7: Platform Features
High rate, precision platform for target tracking.
Direct drives
Support for multiple sensors (COTS)
  Optical cameras
  IR cameras
  Radar
Permanent, Semi-portable or portable deployable onto pre-prepared plinths.
Self calibrating.
Auto-track capability

## Slide 8: USP U42
Rate: > 100 deg/s
Acceleration: > 100 deg/s2
Bandwidth: > 15 Hz
Resolution: < 0.04 arc-sec
Update rate: 1 kHz
T42 Accuracy: 3 to 5 arc-sec
System Acc’y: < 20 arc-sec

## Slide 9: USP U42

## Slide 10: USP T33 Performance
Rate: > 120 deg/s
Acceleration: > 120 deg/s2
Bandwidth: > 15 Hz
Resolution: < 0.04 arc-sec
Update rate: 1 kHz
T33 Accuracy: 3 to 5 arc-sec
System Acc’y: < 20 arc-sec

## Slide 11: Development Platform (COATS)

## Slide 12: COATS with 8” Telescope
Three sensors:
  7 to 0.78 deg FOV, 75 mm
  0.5 deg FOV, 100 mm
  0.24 deg FOV 205 mm
Richey-Chretien 8” telescope
  With filter wheel
    (720 760 800 850 950 1000 nm LP filters)

## Slide 13: Sensor Networking

## Slide 14: Sensor Networking
CL2 Developed
  Real-time Client-Server protocol (MEP)
  Chilbolton 25 m Radar Antenna server (Gandalf)
  Client for COATS
  Client for SGF at Herstmonceux (under development with the SGF)
Demonstrated operation between COATS & Chilbolton radar (CASTR)
  7th Match 2016

## Slide 15: Radar Cueing/Slaving
25 m Antenna Server (Gandalf) accepts inputs from multiple sensors using MEP

## Slide 16: Network Development
Gandalf
Client
MEP

## Slide 17: Network Development
Gandalf
Client
MEP
Client
MEP

## Slide 18: Network Development
Gandalf
Client
MEP
Client
MEP
Gandalf #2
MEP

## Slide 19: Network Development
Gandalf
Client
MEP
Client
MEP
Gandalf #2
MEP
MEP

## Slide 20: Network Development
Gandalf
Client
MEP
Client
MEP
Gandalf #2
MEP
MEP
Client
MEP

## Slide 21: GEO & MEO Observations

## Slide 22: GEO & MEO Observations
Results of observations with CL2 Observation And Tracking System (COATS):
18th to 20th July 2016
15th August 2016
28th & 29th November 2016

## Slide 23: Selected GEOs & MEOs
GEOs
  Skynet 6
  Astra 16
  Inmarsat 3
  LUCH 1
  SES 1
  Hylas 2
MEOs / IGSO
  Galileo 8
  GPS 9
  Bediou 4
  GLONASS 9

## Slide 24: Skynet 4C

## Slide 25: Skynet 4E & 4F
Notes: Separation ~ 50km

## Slide 26: Skynet 5C

## Slide 27: Astra 1KN, 1L, 1M, 1N: 19.2° E

## Slide 28: Astra 1KN, 1L, 1M, 1N: 19.2° E

## Slide 29: Astra Sequence

## Slide 30: Giove A

## Slide 31: Inmarsat 3-F2

## Slide 32: Galileo FM2

## Slide 33: Galileo FM3

## Slide 34: Galileo FM4

## Slide 35: In Summary
Networking of Sensors demonstrated
GEO & MEO observations possible with
  8” aperture telescope
  Sensitive camera
  Favourable phase angles
  Favourable position of the Moon

## Slide 36: Thank you